## Slide 1: A good start to Match Race
Guide on boat handling of a DS37 match racer
v1.0​

## Slide 2: Crew Positions
Roles
Helmsman
Mainsheet
Trimmer
Tailer
Bowman
Work zones
Optimal positioning in the zone
Remain in your zone during maneuvers
While training do not help others in their tasks
Focus on your own responsibility

## Slide 3: Helmsman
Responsibility
Steer
Speed
Timing
Positioning of the boat
Communication if boat should sail with reduced speed
backstay
Tips
Have the best overview of the prestart
Control the speed precisely
Think one step ahead

## Slide 4: Mainsheet
Responsibility
Mainsail sheet
Trim of the boat
Cleaning up in downwind
Winward spinnaker sheet in set
Frontsail halyard up in downwind
Control roll turnings
Communicate laylines
Communicate opponent's speed, height and maneuvers
Overhal Port side frontsail sheet after first gybe
Tips
Trim the boat fast in the prestart
Be aware and communicate about wind power and wind jump before the pre start
Communicate about the advantages of start marks
Best mainsheet exchange
Help the helmsman with tactics
Trim main outhaul and cunningham in downwind if there is time

## Slide 5: Trimmer
Responsibility
Fronsail trim
Frontsail trim in prestart
Help behind the tailer
Sheet points
Spinnaker trim
Barberhauler trim
Drop frontsail halyard in the spinnaker set
Remove frontsail starboard sheet after spinnaker set
Tips
Trim front sail in cooperation with mainsail trimmer
Communicate about frontsail is all in for close hauled, use %
Inform about wind changes, count down
Communicate power in the spinnaker
Loft relievers so they are ready to be relaxed

## Slide 6: Tailer
Responsibility
Tail front sail
Spinnaker windward sheet
Barberhauler
Mainsail and frontsail halyard
Cunningham and kick
Spinnaker pole up and down
Spinnaker halyard
Cleaning up in the cockpit
Flying spinnaker pole
Spinnaker drop
Hold the boom out in downwind
Tips
Save your energy
Explode in tailing
Down on knees
Drop the halyard in spinnaker drop, if panic drop help the bowman and return on tail, get ready for fast turnings and control the kick
Clean up in the boat

## Slide 7: Bowman
Responsibility
Foredeck
Time keeping
Y-flag in the protest
Kick
Spinnaker pole up and down
Halyards on mast
Spinnaker set
Call frontsail up in downwind
Call spinnaker pole down
Tips
Sense of order on foredeck
Orientation of the leeward mark on downwind
Count down to prestart and start for the helmsman